## Slide 1: Manager-Client Pairing: A Framework for Implementing Coherence Hierarchies
Jesse G. Beu
Michael C. Rosier
Thomas M. Conte
Tinker Research
Georgia Institute
of Technology

## Slide 2: The Problem
Coherence protocols can be difficult to design properly
Integration of coherence protocols is even more difficult
Leads to monolithic, homogenous coherence in a heterogeneous future
Directory MESI

## Slide 3: The Solution
Use existing protocols as building blocks
Enable coherence integration and composition
Leads to heterogeneous hierarchies in a heterogeneous future
  Design using best local protocol for the ‘common case’
Directory MESI
Broadcast
MSI
Broadcast
MSI
Token Rings

## Slide 4: Width Variation Observation
Ocean_C while varying tier width at fixed 2-level
L2 Hit
Off-Chip

## Slide 5: Manager-Client Pairing
Notes: Divides responsibility between Client and Manager
Pair a Client from one protocol with the manager of the next
  Client becomes a gateway for the lower coherence realm
  MCP defines protocol-to-protocol communication

## Slide 6: Outline
Motivation
Introduce Manager-Client Pairing
Communication Similarity and Recursion
Types of Action
  Query, Get and Grant
MCP Algorithm and Example
Impact of Tier Width and Hierarchy Height
Future Work and Conclusion

## Slide 7: Self-Similarity for Recursion
Processor <-> Cache
  Request Data
    Transparently asks if we have permission
    Gets permission if not
  Cache supplies Data
Cache <-> Memory
  Request Data
  Memory supplies Data
  Add ‘asking’ feature
Internals of each layer can be ‘black-boxed’

## Slide 8: Types of Actions
Query – Permission Query to check permission level
Get – Request permissions and Data
  Read and Write Permission, supplying Data
  Permission upgrade (e.g. Shared -> Modified)
Grant – Response to earlier Get request
Notes:   Boolean, returning true if permission is sufficient
  Support for ‘eviction permission’ check (e.g. dirty data, owner, etc.)
  Read and Write Permission, supplying Data
  Permission upgrade (e.g. Shared -> Modified)
  Eviction handling logic when manager needs to be notified
  In blocking protocols, upon reception causes final acknowledge to be issued back to Manager
  Signifies completion from the Client perspective

## Slide 9: Manager and Client Pair

## Slide 10: MCP Algorithm
Load
Get
Grant
Processor

## Slide 11: Example – Realm Hit

## Slide 12: Example – Realm Miss
Downgrade
I
I
I
I
E
M
M

## Slide 13: Latency Impact of Hierarchies
Strong analogy with cache design
  Tier width (# of clients) <-> cache sizing
    Smaller Tiers result in ‘lower capacity’ with ‘faster access’
    Larger Tiers have ‘higher capacity’ with ‘slower access’
  Hierarchy height (# of tiers) <-> cache levels
    Motivation of this work!
      Single flat protocol won’t scale
      Analogous to having a monolithic cache
    Deeper hierarchies are not always good
      Benefit of smaller, fast tiers while retaining capacity
      Make too small and the lowest level will frequently miss
      Additional penalty of hierarchy indirection
    Consider L3/L4 Caches vs. larger L2/L3 caches

## Slide 14: Tier Width
Home Node
Realm Hit
Realm Miss

## Slide 15: Width Variation Observation
Ocean_C while varying tier width at fixed 2-level

## Slide 16: Future Work
MCP’s role in Validation
  Willing to discuss off-line
Protocol interactions/selection
Protocol and NOC topology co-design
  Hierarchical topologies
Cross-vendor coherence integration

## Slide 17: Conclusion
MCP does address concerns regarding future coherence
  Uses existing protocols as building blocks
  Enables coherence integration and composition
  Demonstration of rapid development of a variety of hierarchy configurations
  MCP provides a generic coherence hierarchy composition framework to support continued scaling of diverse, massively coherent systems

## Slide 18: Questions?
Thank you!